## Slide 1: Reducing Memory Reference Energy with Opportunistic Virtual Caching
Arkaprava Basu
Mark D. Hill
Michael M. Swift
University of Wisconsin-Madison

## Slide 2: Executive Summary
TLB is energy hungry
  TLB lookup on each access due to Physical Caching
  TLB latency hiding makes L1 cache energy worse
Virtual Caching could help
  But read-write synonyms
  ISA-specific incompatibility etc.
Virtual Caching problems are real but rare
Opportunistic Virtual caching
  Best of Virtual and Physical Caching

## Slide 3: Outline
Motivation and Goal
  TLB Energy hungry
  Physical Caching
  Problems of Virtual Caching
Opportunities for Virtual Caching
Mechanisms for Opportunistic Virtual Caching
Evaluation
Summary

## Slide 4: TLB is Energy Hungry
~3-13% of “core” power due to TLB [Sodani, MICRO’11 Keynote]
We find TLB contributes 6.6-13% on-chip memory’s dynamic energy
TLB shows up as hotspot [Puttaswamy, VLSI ‘06]
* From Sodani’s /Intel’s MICRO 2011 Keynote
13%

## Slide 5: Why is TLB energy hungry?
TLB looked up on every cache access
  ALL blocks cached with physical address
  Each access needs address translation
TLB lookup latency in critical path
  Fast and thus energy hungry transistors
  Content Addressable Memory

## Slide 6: TLB Latency Hiding Constrains L1 Associativity
Virtually Indexed Physically Tagged L1 Caches
  L1 Assoc. >= Cache Size/Page Size; e.g., 32KB/4KB => 8-way
Tag matching logic
L1 Cache (32KB, 8 way)
TLB
Way0
Way4
Way7
VA46 ………………… VA0
Page offset

## Slide 7: TLB Latency Hiding Makes L1 Energy Worse
Dynamic Energy | 4-way | 8-way | 16-way
Read Energy | 1 | 1.309 | 1.858
Write Energy | 1 | 1.111 | 1.296
Workloads | 4-way | 8-way | 16-way
Parsec | 1 | 1.002 | 1.002
Commercial | 1 | 1.002 | 1.004
Relative L1 Access Energy
Relative Performance
Substantial energy impact dominates negligible performance benefit of increased associativity
*Methods: CACTI, full system simulation

## Slide 8: Why Not Virtual Caching?
Cache ALL blocks under virtual address
  Saves TLB lookup on L1 cache hits
  L1 Cache associativity not constrained
  Read-Write Synonyms
    e.g, V1 -> P0 <- V2
  Incompatibility with commercial ISAs
    e.g., x86 ‘s hardware page table walker
  and many more…
Best of Virtual and Physical Caching?
Notes: Should I have short animation describing the issue?

## Slide 9: Outline
Motivation and Goal
Opportunities for Virtual Caching
Mechanisms for Opportunistic Virtual Caching
Evaluation
Summary

## Slide 10: How Frequent are Synonyms?
Applications | Static Synonym Pages | Dynamic accesses to Synonyms
canneal fluidanimate facesim streamcluster swaptions x264 | 0.06% 0.28% 0.00% 0.23% 5.90% 1.40% | 0% 0% 0% 0.01% 26% 1%
bind firefox memcached specjbb | 0.01% 9% 0.01% 1% | 0.16% 13% 0% 2%
Synonyms occur, but conflicting use rare; confined to small region.
Parsec
Commercial
100%
95%
Read-only

## Slide 11: Identify Synonyms at Allocation?
Process address space divided into regions
Synonym possibility indicated by protection flags
OS knows where in the memory page tables are located
Code
Constants
Stack
Heap
Sys V
r-x--
r----
r-w--
r-w-s
r-w--
-----
Possible to separate memory regions with and without read-write synonyms
Protection flags
r-> read
w-> write
s->shared
x->execute
System V Shared Memory

## Slide 12: Insights and Idea
Recap:
  Physical Caching energy hungry
  Virtual Caching can be energy efficient, But hard
  Read-write synonyms occur but rare
  OS knows where read-write synonyms possible
 Opportunistic Virtual Caching
  Virtual Caching when opportunity exists
  Default to Physical Caching when needed

## Slide 13: Outline
Motivation and Goal
Opportunities for Virtual Caching
Mechanisms for Opportunistic Virtual Caching
  Role for Hardware and Operating System
  Physical Caching in Opportunistic Virtual caching
  Virtual Caching in Opportunistic Virtual caching
  Operating System support
Evaluation
Summary

## Slide 14: Role of the H/W and the OS
Hardware allows Virtual or Physical Caching
OS decides when to use Virtual Caching
OS responsible for correctness

## Slide 15: Physical Caching in Opportunistic Virtual Caching
Tag matching logic
L1 Cache (32 KB, 8Way)
TLB
Way0
Way4
Way7
0 = VA47 VA46 ……………… VA0
Virtual Addr.
NO
ovc_enable
(Default Off)
Notes: Should we show example to make people understand how the tag matching work?

## Slide 16: Virtual Caching in Opportunistic Virtual Caching
Tag matching logic
L1 Cache (32 KB, 4-way/8-way)
TLB
Way0
Way4
Way7
1 = VA47 VA46 ……………… VA0
Virtual Addr.
Yes
ovc_enable
DATA
(V/P) TAG
Permission bits
ASID
Physical
Tag
Notes: How to show the TAG match?

## Slide 17: Operating System Mechanisms
Memory allocations from two partitions
  Separate partitions for virtual and physical caching
    e.g., VA47= 0 =>Physical Caching and VA47= 1 => Virtual Caching
  Protection flags determine which partition to use
Operating System responsible for correctness
  Wrong classification possible, but rare
    e.g., User makes a region shared after allocation
  Cache flush on possible violation

## Slide 18: Outline
Motivation and Goal
Opportunities for Virtual Caching
Mechanisms for Opportunistic Virtual Caching
Evaluation
  Methodology
  Results
  Overheads
Summary

## Slide 19: Methodology
Modification to Linux kernel (2.6.28-4)
  < 300 LOC changes among hundreds thousands LOC
Hardware changes simulated in gem5 full-system simulator
Energy numbers from CACTI

## Slide 20: Configuration
Cores | 4 cores, in-order, x86-64 ISA
TLBs | L1 DTLB/ITLB 64 entries, Fully associative, L2 TLB 512 entries, 4-way set associative
Privates Caches | 32 KB 8way I/D-L1 cache, 256 KB , 8-way L2 per core
Shared Caches | 8MB, 16-way L3 cache
Memory | 4 GB memory 300 cycles round trip

## Slide 21: Dynamic Energy Savings?
Chart: % of on-chip memory subsystem's dynamic energy
| canneal | facesim | fluidanimate | streamcluster | swaptions | x264 | specjbb | memcached | bind | Mean
L2+L3 Energy | 65.3464 | 0 | 0 | 42.8235 | 0 | 0 | 6.912 | 0 | 0 | 48.0681 | 0 | 0 | 1.164 | 0 | 0 | 28.9694 | 0 | 0 | 46.8966 | 0 | 0 | 50.0546 | 0 | 0 | 10.5721 | 0 | 0 | 40.0795 | 0
L1 Energy | 30.1052 | 0 | 0 | 49.6545 | 0 | 0 | 80.7735 | 0 | 0 | 45.1203 | 0 | 0 | 85.7329 | 0 | 0 | 61.1505 | 0 | 0 | 45.9879 | 0 | 0 | 43.3335 | 0 | 0 | 77.602 | 0 | 0 | 51.9551 | 0
TLB Energy | 4.5483 | 0 | 0 | 7.522 | 0 | 0 | 12.3145 | 0 | 0 | 6.8116 | 0 | 0 | 13.1031 | 0 | 0 | 9.8801 | 0 | 0 | 7.1155 | 0 | 0 | 6.6119 | 0 | 0 | 11.8259 | 0 | 0 | 7.9653 | 0
L2+L3 Fraction | 0 | 65.3227 | 0 | 0 | 42.8348 | 0 | 0 | 6.9025 | 0 | 0 | 48.0664 | 0 | 0 | 1.2095 | 0 | 0 | 28.7196 | 0 | 0 | 46.7249 | 0 | 0 | 49.7527 | 0 | 0 | 11.5347 | 0 | 0 | 40.0405
L1 Fraction | 0 | 24.0569 | 0 | 0 | 38.4693 | 0 | 0 | 62.3862 | 0 | 0 | 24.7619 | 0 | 0 | 66.1841 | 0 | 0 | 45.5672 | 0 | 0 | 35.4107 | 0 | 0 | 33.257 | 0 | 0 | 59.9103 | 0 | 0 | 40.1335
TLB Fraction | 0 | 0.63133 | 0 | 0 | 0.12088 | 0 | 0 | 0.039283 | 0 | 0 | 0.16767 | 0 | 0 | 0.064402 | 0 | 0 | 0.26721 | 0 | 0 | 0.31738 | 0 | 0 | 0.2253 | 0 | 0 | 0.272 | 0 | 0 | 0.27998
Physical Caching
(VIPT)
Opportunistic Virtual Caching
On average ~20% of the on-chip memory subsystem’s dynamic energy is reduced

## Slide 22: Overheads
No significant performance overhead
  Average performance degradation 0.017%
State overhead
  27.5KB extra state for ~9.25 MB cache hierarchy (< 0.3%)
  < 1% static power overhead
No significant state or static power overheads but significant dynamic power savings

## Slide 23: Outline
Motivation and Goal
Observation and Opportunity
Mechanisms
Results
Related Work and Conclusion

## Slide 24: Related Work
Virtual Caching
  In-cache address translation [Wood’86]
  TLB energy reduction using Virtual Caching [Ekman’02]
  Bloom filter for synonym lookup [Woo’06]
TLB structure optimizations
  Hardware Translation register [Kadayif’07]
  Hardware filter to buffer access [Chang’07]
Software aided TLB optimizations
  TLB static portioning for memory regions [Lee’03]
  Heterogeneous tagged cache [Zhou’08]

## Slide 25: Summary
TLB energy dissipation non-negligible
TLB latency hiding makes L1 energy worse
Virtual Caching could help, but hard
  Read-Write Synonym can occur but rare
  OS can find where read-write synonym possible
Opportunistic Virtual Caching
  Best of both Virtual and Physical Caching
    Virtual Caching for power savings
    Physical caching for compatibility

## Slide 26
Thank you

## Slide 27
Backup

## Slide 28: How Coherence is Maintained?
0x10ab16e10 (VA)
0x10ab16e10
0x00fc10d10
(PA)
0x00fc10d10
(PA)
TLB
L1 Cache
To lower level caches
0x10ab16e10 (VA)
MSHR
CASE 1. Coherence reply due to own request
Miss
4
4

## Slide 29: How Coherence is maintained?
L1 Cache
CASE 2. Coherence request due to other controller
Physical Tag array
0x00fc10d10
(PA)

## Slide 30: Alternative techniques for address differentiation?
Range register(s) for Virtual Caching
≥
≤
0xfff10000100 (VA)
0xfff10000000
0xfff10f00000
Lower bound
Upper bound
1= Use Virtual Caching 0= Use Physical Caching

## Slide 31: What about static power?
Around 42-45% of the total on-chip memory subsystem power
 OVC can save around 12% of total on-chip memory subsystem’s power

## Slide 32: What is the breakup of TLB lookup savings?
 | L1 Data TLB | L1 Instr. TLB
canneal | 72.253 | 99.986
facesim | 96.787 | 99.999
fluidanimate | 99.363 | 99.999
streamcluster | 95.083 | 99.994
swaptions | 99.028 | 99.989
x264 | 95.287 | 99.304
specjbb | 91.887 | 99.192
memcached | 94.580 | 98.605
bind | 97.090 | 98.310
Mean | 93.484 | 99.486