## Slide 1: Efficient Virtual Memory for Big Memory Servers
Arkaprava Basu, Jayneel Gandhi, Jichuan Chang*, Mark D. Hill, Michael M. Swift
  “Virtual Memory was invented in a time of scarcity. Is it still good idea?”
  --- Charles Thacker, 2010 Turing Award Lecture
* HP Labs
Notes: Chuck Thacker asked in his 2010 Turning award lecture “Virtual Memory was invented in a time of scarcity. Is it still good idea?” ..We explore this question in the context of big memory workloads

## Slide 2: Executive Summary
Big memory workloads important
  graph analysis, memcached, databases
Our analysis:
  TLB misses burns up to 51% execution cycles
  Paging not needed for almost all of their memory
Our proposal: Direct Segments
  Paged virtual memory where needed
  Segmentation (No TLB miss) where possible
Direct Segment often eliminates 99% DTLB misses
Notes: The emerging big memory workloads like graph analytics, in-memory cache and also databases that uses 100GBS to TBs of memory can spend considerable number of cycles serving TLB misses.
But more interestingly we find that often many of the rich features of paged Virtual Memory is not used by these workloads, while the hardware like x86, ARM accesses all memory through paged virtual memory.
To address this mismatch between we propose direct segment where a part of memory usage can use segmentation that incurs no TLB miss. This enables fast address translation for memory usage that does not benefit from paging. Rest of the memory can use conventional page virtual memory where needed w

## Slide 3: Virtual Memory Refresher
Core
Cache
TLB
(Translation Lookaside Buffer)
Process 1
Process 2
Virtual Address Space
Physical Memory
Page Table
Challenge: TLB misses wastes
execution time
Notes: Before we delve into details a quick refresher on virtual memory to make sure I have all on board
Software generates virtual addresses as it accesses memory
Each procsess has its own virtual address space.
This VA gets mapped to PA at the granulairty of page. A common grain is 4KB in x86
The mapping information is stored hierarchal page table
Now since each memory access needs a translation needs a translation, processors used a hardware cache called TLB or translation look aside buffer.
Hits to TLB is fast but on miss a page-table walker walks the page table that could several sycles.
The goal is to reduce this TLB misses.
While such a TLB design remained unchanged for several decades memory usage has changed significantly

## Slide 4: Memory Usage Trend
Memory Size: MB GB TB
  Windows Server: 64GB 4TB in a decade
TLB size remained almost constant
Low access locality of server workloads [Ramcloud’10]
  TLB is less effective
Memory Size + TLB size => TLB miss overhead
Year | 1999 | 2001 | 2008 | 2012
L1-DTLB entries | 72 (Pent. III) | 64 (Pent. 4) | 96 (Nehalem) | 100 (Ivy Bridge)
Notes: Recently there has been trend of increasing TLB overhead. There are a many reasons behind it.
First and foremost, ever increasing memory footprint of software coupled with decreasing cost per bit of DRAM meant that the installed memory of especially server systems has grown from MBs to GBs and now TBs.
Whereas the TLB hasn’t grown at the same pace due to obvious power and latency budget as TLB is in critical path of every memory access. For example in Intel processors total number of TLB entries has grown from 72 in early 2000s to 100 today.
Further recent large memory workloads increasingly demonstrate less access locality and TLB like anyother cache needs access locality to produce cache hits.

## Slide 5: Experimental Setup
Experiments on Intel Xeon (Sandy Bridge) x86-64
  Page sizes: 4KB (Default), 2MB, 1GB
96GB installed physical memory
Methodology: Use hardware performance counter
 | 4 KB | 2 MB | 1GB
L1 DTLB | 64 entry, 4-way | 32 entry, 4-way | 4 entry, fully assoc.
L2 DTLB | 512 entry, 4-way |  | 
Notes: To understand how TLB misses can incur substantial problem even today we ran experiment on real hardware which in this case is Intel Xeon based on 32nm Sandy bridge architecture.
This micro architecture support 3 page sizes, 4KB which is the default page size and also enable two larger page sizes 2MB and 1GB. Larger page size maps the larger contiguous virtual address to contiguous physical address and can help reduce TLB misses my allowing same number of TLB entries to map larger amount of memory.
The TLB hierarchy for different page sizes are as shown in the table.
Separate TLBs for different page size and base page sizes have two levels of TLB.
96 GB of installed installed memory, unfortunate not TBs.
And for measurement we used hardware performance counters.

## Slide 6: Big Memory Workloads
Notes: We selected the workloads that generally run on server side of things and use lot of memory.

## Slide 7: Execution Time Overhead: TLB Misses
Notes: Y axis we have the percentage of execution cycle spent on servicing Data-TLB misses
As we can see some workloads can spent significant fraction of cycles on TLB misses upto 51 % for graoh500

## Slide 8: Execution Time Overhead: TLB Misses
Notes:                 If 2MB pages are used the overheads moderate and can

## Slide 9: Execution Time Overhead: TLB Misses
Notes: First lets see whether the problem actually exists or not.
A set of workloads, first column shows how many cycles hardware page table walker in a 32 nm Sandybridntge/westmere machine spends as percentage of the execution time.
Second column shows number of L1 + L2 TLB misses experienced per 1K instructions
More interestingly when we do the same experiment on non-server things are very different

## Slide 10: Execution Time Overhead: TLB Misses
Significant overhead of
paged virtual memory
Worse with TBs of memory now or in future?
Notes: First lets see whether the problem actually exists or not.
A set of workloads, first column shows how many cycles hardware page table walker in a 32 nm Sandybridntge/westmere machine spends as percentage of the execution time.
Second column shows number of L1 + L2 TLB misses experienced per 1K instructions
More interestingly when we do the same experiment on non-server things are very different

## Slide 11: Execution Time Overhead: TLB Misses

## Slide 12: Roadmap
Introduction and Motivation
Analysis: Big memory workloads
Design: Direct Segment
Evaluation
Summary
Notes: To understand the opportunities to optimize for these workloads we begin by analyzing how memory is used by them

## Slide 13: How is Paged Virtual Memory used?
Client
memcached server # n
In-memory Hash table
Key X
Value Y
Network state
An example: memcached servers
Notes: First we take an example of memcached which is a in-memory object cache accessed over the network.
It uses up most of its memory for gigantic in-memory hash table with uniform permission, while small fraction uses for things like network connections
Similar in many other applications that uses lot of memory---they have a gigantic data structure that accounts for most of its memory usage and ut hgas some interesting implications to virtual memory usage.

## Slide 14: Big Memory Workloads’ Use of Paging
Paged VM Feature | Our Analysis | Implication
Swapping | ~0 swapping | Not essential
Per-page protection | ~99% pages read-write | Overkill
Fragmentation reduction | Little OS-visible fragmentation (next slide) | Per-page (re)-allocation less important
Notes: So lets see what this means for for the virtual memory system
We would start by looking into each of key features that page based Virtual memory enables
First lets think of swapping. Swapping is the process of transparently transfer pages between the memory and the disk. In the days when physical memory was scarce this gave an illusion of larger memory than actually.
But the current workloads are configured to fit into physical memory to avoid long latency swap operation.
Then page based virtual memory enables fine grain page protection but for all most all of the memory allocated contains uniform read write permission. This raises the question do you need fine grain memory protection
Paging can help contain external fragmentation by allocating memory in fixed sized grain. If memory is allocated and de-allocated in many different sizes external fragmentation can thrive where physical memory can be scattered in holes and could be wasted if many allocation and deallocation. However as we will see soon these workloads request memory upfront from the OS and then manage it themselves. Thus OS does not have a big role to minimize the fragmentation.

## Slide 15: Memory Allocation Over Time
Chart: 
Warm-up
Most of the memory allocated early
Allocated Memory (in GB)
Time (in seconds)
Notes: In thus slide on x axis we plot execution time in seconds while the Y axis shows the Allocated memory in GB
We see that after initial allocation the memory usage stabilizes. This also makes the it easier to predict the memory requirement for running these big memory workload
So we this far we have seen that few of the key features of the traditional page-based virtual memory many not crucial for big memory workloads for most part. So the obvious question is where it is useful to have it

## Slide 16: Where Paged Virtual Memory Needed?
Dynamically allocated
Heap region
Paging Valuable
Paging Not Needed
Code
Constants
Shared Memory
Mapped Files
Stack
Paged VM not needed for MOST memory
Guard Pages
VA
* Not to scale
*
Notes: 1. For example code section or mapped files, shared memory, guard pages etc. but they correponds to small portion of the memory usage
Not to mention we have ben concentrating on big memory workload running on the system but there would be 100s of other minor processes at any given point of time and they can remain un altered.

## Slide 17: Roadmap
Introduction and Motivation
Analysis: Big Memory Workloads
Design: Direct Segment
  Idea
  Hardware
  Software
Evaluation
Summary
Notes: Based on this observation we will try to find a minimalistic solution that could address the mismatch between the what application needs and what the system provides.

## Slide 18: Idea: Two Types of Address Translation
Conventional paging
    All features of paging
    All cost of address translation
  Simple address translation
    NO paging features
    NO TLB miss
OS/Application decides where to use which [=> Paging features where needed]
A
B
Notes: We simply provide two types memory address translation for no-overlapping regions of virtual address space
First the conventional access through paged memory. All features of paging and its cost
Second a fast address translation that woulc not incur TLB miss but restricted in usage
And the OS/Application decides which type of memory access to use for what type of memory
Next we will first try to get an understanding of how two types of memory access is enabled in the hardware

## Slide 19: Hardware: Direct Segment
OFFSET
BASE LIMIT
VA
Conventional Paging
PA
1
2
Direct Segment
Why Direct Segment?
  Matches big memory workload needs
  NO TLB lookups => NO TLB Misses
Notes: First virtual address space can be mapped to physical addresses using conventional paging. Blue rectangles are pages here.
We introduce a form of segmentation that could map an arbitrarily large contiguous region of VA space to a contiguous physical address.
To do this we introduce three registers per core.
BASE and LIMIT registers delineate VA region to mapped by Direct Segment while Offset register allows calculating PA from VA without any lookup.
So obvious question is why Direct Segment can be preferable way of address translation?
Next we step by step process how a virtual address is translated in presence of direct segment hardware

## Slide 20: H/W: Translation with Direct Segment
[V47V46……………………V13V12]
OFFSET
[P40P39………….P13P12]
DTLB Lookup
Page-Table Walker
Y
MISS
[P11……P0]
BASE ≥?
LIMIT<?
HIT/MISS
[V11……V0]
Paging Ignored
Notes: First the page offset remains unchanged between the virtual address and the physical address
So what is of interest is virtual page number to physical page frame number translation
For that DTLB lookedup in parallel to the BASE and LIMIT registers.
Let us first assume that the VA to be translated falls within the BASE and LIMIT value. If so the physical page number is found simply by adding the value of the OFFSET register to the VA.
And on the other side DTLB lookup would miss since no traslation is available but a the page table walk would be turned off to essentially ignoring the paging

## Slide 21: H/W: Translation with Direct Segment
[V47V46……………………V13V12]
OFFSET
[P40P39………….P13P12]
DTLB Lookup
Page-Table Walker
N
MISS
[P11……P0]
BASE ≥?
LIMIT<?
HIT/MISS
[V11……V0]
Direct Segment Ignored
HIT
Notes: If however the address is not within the BASE and LIMIT register values then it ignores the Direct Segment
On the other side of the things the translation can be found in the TLB which is fast and if not then the page table walker is triggered.
So what we see till now that hardware allows a fast address translation of a contiguous section of virtual address space to a contiguous physical memory while rest of of the address space can be used for paging.
However to make the application take advantage of this the OS needs to play a crucial part

## Slide 22: S/W: Setup Direct Segment Registers
BASE LIMIT
Calculate register values for processes
  BASE = Start VA of Direct Segment
  LIMIT = End VA of Direct Segment
  OFFSET = BASE – Start PA of Direct Segment
Save and restore register values
1
OFFSET
PA
VA1
VA2
Notes: To map a portion of the VA through DS it needs to setup the h/w registers first
These values of these registers are part of process metadata and thus saved and restored on context switch just like page table root pointer.

## Slide 23: S/W: Provision Physical Memory
Create contiguous physical memory
  Reserve at startup
    Big memory workloads cognizant of memory needs
    e.g., memcached’s object cache size
  Memory compaction
    Latency insignificant for long running jobs
      10GB of contiguous memory in < 3 sec
      1% speedup => 25 mins break even for 50GB compaction
2
Notes: Second, direct segment needs contiguous physical memory and the OS is responsible for ensuring that.
Contiguous physical memory can be created by reservation. While reserving memory seems tricky in general, we find that for the class of big memory workload we focus the memory needs are already part of their run configuration .
For example memcached’s cache size is part of the runtime parameter
Contiguous memory can be dynamically created through compaction and Linux supports compaction. While compaction often deemed too costly, but for the long running workloads we focus that runs compaction cost can be easily amortized.

## Slide 24: S/W: Abstraction for Direct Segment
Primary Region
  Contiguous VIRTUAL address not needing paging
  Hopefully backed by Direct Segment
  But all/part can use base/large/huge pages
What allocated in primary region?
  All anonymous read-write memory allocations
  Or only on explicit request (e.g., mmap flag)
3
VA
PA
Notes: Next more subtle responsibility is to provide abstraction fro direct segment. We call the s/w abstraction as primary region.
It’s a contiguous virtual address region that may not benefit from paging.
All or part of primary region could be backed by Direct Segment so paging features are not guaranteed for memory allocations in the primary region. However conventional paging could also be used to map primary region. This can be helpful if under memory pressure memory need to be swapped up then a direct segment can be concerted to paging and then swapped up as usual.
Next obvious question is which memory allocation gets onto the primary region.
We found that dynamically allocated memory with read-write region are most conducive to be mapped onto primary region. Other models whether application could be asked to explicitly request allocation on primary region is possible as well.
Finally since VA space is abundant in 64 bit OS, we overprovision the primary region in a process’s VA space as 4TB long so that it can accommodate largest possible Direct Segment.

## Slide 25: Roadmap
Introduction and Motivation
Analysis: Big Memory Workloads
Design: Direct Segment
Evaluation
  Methodology
  Results
Summary

## Slide 26: Methodology
Primary region implemented in Linux 2.6.32
Estimate performance of non-existent direct-segment
  Get fraction of TLB misses to direct-segment memory
  Estimate performance gain with linear model
Prototype simplifications (design more general)
  One process uses direct segment
  Reserve physical memory at start up
  Allocate r/w anonymous memory to primary region

## Slide 27: Execution Time Overhead: TLB Misses
Lower is better

## Slide 28: Execution Time Overhead: TLB Misses
Lower is better

## Slide 29: Execution Time Overhead: TLB Misses
99.9%
99.9%
92.4%
99.9%
99.9%
99.9%
“Misses” in Direct Segment
Lower is better

## Slide 30: (Some) Limitations
Does not (yet) work with Virtual Machines
    Can be extended but memory overcommit challenging
Less suitable for sparse virtual address space
One direct segment
  Our workloads did not justify more

## Slide 31: Summary
Big memory workloads
  Incurs high TLB miss cost
  Paging not needed for almost all memory
Our proposal: Direct Segment
  Paged virtual memory where needed
  Segmentation (NO TLB miss) where possible

## Slide 32
Thank You
&
Questions?

## Slide 33
BACKUP

## Slide 34: Address Translation in Different ISA/machines
ISA/Machine | Address Translation
Multics | Segmentation on top of Paging
Burroughs B5000 | Segmentation
UltraSPARC | Paging
X86 (32 bit) | Segmentation on top of Paging
ARM | Paging
PowerPC | Segmentation on top of Paging
Alpha | Paging
X86-64 | Paging only (mostly)
Direct Segment:
  NOT on top of paging.
  NOT to replace paging.
  NO two-dimensional address space. Keeps Linear address space.

## Slide 35: Why not Huge Pages?
Huge pages does not automatically scale
  New page size and/or more TLB entries
TLBs dependent on access locality
Fixed ISA-defined sparse page sizes
  e.g., 4KB, 2MB, 1GB
  Needs to be aligned at page size boundaries
Multiple page sizes introduces TLB tradeoffs
  Fully associative vs. set-associative designs

## Slide 36: Direct Segment in Cloud?
In current incarnation DS most suitable for enterprise workloads
  Less suitable when many short jobs come and go
Memory usage needs to be predictable to enable performance guarantees
  Same memory usage predictions can be used to create DS

## Slide 37: How to handle faulty pages?
Direct segment can not remap faulty pages
  No ability to remapping at small granularities
Revert part or all of direct segment memory
Memory controller remaps faulty pages
  Only small number of faulty pages
  List of faulty re-mapped pages in MC

## Slide 38: Methodology
S/W TLB miss tracker
  Make PTEs invalid in memory valid in TLB
  Trap to OS on each TLB miss
  Range checking against direct segment’s VA
Assumption
  TLB miss overhead reduces proportionally with the number of DTLB misses