## Slide 1: How to snapshot memory
Vinod Ganapathy
vg@iisc.ac.in
securely

## Slide 2: The layer-below principle
User
app
Memory
I/O devices
CPU
Hardware
Operating
System
Syscalls
Process
List
Kernel
Code
IDT
…
User
app
Utilities &
Libraries
ls, ps, &
bash utilities
libc
gcc
…
…
The lower you go, the more control you have
Least control
Most control

## Slide 3: Example: Malware detection
User
app
Hardware
Operating
System
Utilities &
Libraries

## Slide 4: Example: Malware detection
User
app
Hardware
Operating
System
Malware detector
Utilities &
Libraries

## Slide 5: Example: Malware detection
User
app
Hardware
Operating
System
Malware detector
Utilities &
Libraries
cat
ps
ls
…
TCB
Trusted
Layer

## Slide 6: Libraries may be compromised!
User
app
Hardware
Operating
System
Malware detector
Utilities &
Libraries
cat
ps
ls

## Slide 7: Solution: Query the OS
User
app
Hardware
Operating
System
Malware detector
Utilities &
Libraries
System call API
1
2
3
Query with syscall
OS reads file
Returns true
file content
3
TCB
1
2

## Slide 8: What if the OS is malicious?
User
app
Hardware
Operating
System
Malware detector
Utilities &
Libraries
System call API
Notes: Is it game over?

## Slide 9: How does an OS get infected?
Exploits of kernel vulnerabilities:
  Injecting malicious code by exploiting a memory error in the kernel
Privilege escalation attacks:
  Exploit a root process and use resulting administrative privileges to update the kernel
Social engineering attacks:
  Trick user into installing fake kernel updates
    Defeated via signature verification of kernel updates
    Trivial to perform prior to the Windows Vista OS

## Slide 10: How prevalent are OS infections?
2010 Microsoft report: 7% of all infections from client machines due to rootkits[1]
2016 HummingBad Android rootkit:[2]
  Up to 85 million Android devices infected?
  Earns malware authors $300,000 each week through fraudulent mobile advertisements
Used in many high-profile incidents:
  Torpig and Storm botnets
  Sony BMG (2005), Greek wiretapping (2004/5)
[1] | Microsoft Malware Protection Center, “Some Observations on Rootkits,” January 2010, https://blogs.technet.microsoft.com/mmpc/2010/01/07/some-observations-on-rootkits
[2] | CheckPoint Software, “From HummingBad to Worse,” July 2016, http://blog.checkpoint.com/wp-content/uploads/2016/07/HummingBad-Research-report_FINAL-62916.pdf

## Slide 11: How can we detect OS infection?
User
app
Hardware
Operating
System
Malware detector
Utilities &
Libraries
System call API
Hypervisor (a.k.a. Virtual Machine Monitor)
Ask for help from the layers below
TCB
Notes: Is it game over?

## Slide 12: How low can we go?
User
app
Hardware
Operating
System
Malware detector
Utilities &
Libraries
Hypervisor
[Bluepill, Subvert]
TCB
Notes: Is it game over?

## Slide 13: How low can we go?
User
app
Operating
System
Malware detector
Utilities &
Libraries
Hardware
[Stuxnet, Trojaned ICs]
???
TCB
Notes: Is it game over?

## Slide 14: Today’s talk
Memory forensics: Using memory snapshots to detect system infection.
Volatility Foundation

## Slide 15: Modus operandi
User app
Physical Memory
Hardware
Operating
System
Syscall
Process
List
Kernel
Code
User app
Utilities &
Libraries
…
Target machine
Potentially rootkit-infected
TCB

## Slide 16: Modus operandi
User app
Physical Memory
Hardware
Operating
System
Syscall
Process
List
Kernel
Code
User app
Utilities &
Libraries
…
Target machine
Potentially rootkit-infected
Analysis machine
Trusted
TCB

## Slide 17: Modus operandi
User app
Physical Memory
Hardware
Operating
System
Syscall
Process
List
Kernel
Code
User app
Utilities &
Libraries
…
Target machine
Potentially rootkit-infected
Analysis machine
Trusted
TCB
Snapshot of
memory pages
…

## Slide 18: Research questions
How do we analyze memory snapshots?
  Large body of work (~15 years) on this topic.
How can we snapshot memory pages without involving the target’s OS?
  Focus of this talk!

## Slide 19: Snapshot acquisition mechanism
 | Tamper resistance | Performance isolation | Snapshot consistency
1
2
3

## Slide 20: Tamper resistance
 | Tamper resistance | Performance isolation | Snapshot consistency
Target should not interfere with snapshot acquisition

## Slide 21: Tamper resistance
 | Tamper resistance | Performance isolation | Snapshot consistency
Virtualization |  |  | 
Target should not interfere with snapshot acquisition
Physical Memory
Virtual Hardware
Operating
System
Hypervisor
Hypervisor can fetch memory from virtual machine without OS involvement

## Slide 22: Tamper resistance
 | Tamper resistance | Performance isolation | Snapshot consistency
Virtualization |  |  | 
Co-processor |  |  | 
Target should not interfere with snapshot acquisition
Physical Memory
Hardware
Operating
System
Co-processor uses DMA
OS on target involved in DMA setup
Malicious OS can hide portions of memory with malicious content

## Slide 23: Performance isolation
 | Tamper resistance | Performance isolation | Snapshot consistency
Virtualization |  |  | 
Co-processor |  |  | 
Do not halt the target during snapshot acquisition
Necessary for situations where frequent snapshot acquisition is necessary
Hypervisor-based acquisition requires pausing the virtual machine
Co-processor can operate in concert with target

## Slide 24: Snapshot consistency
Consistent snapshot
Inconsistent snapshot

## Slide 25: Snapshot consistency
 | Tamper resistance | Performance isolation | Snapshot consistency
Virtualization |  |  | 
Co-processor |  |  | 
Snapshot should faithfully represent target’s state at a given instant in time
Physical Memory
Hardware
Operating
System
F1
F2
…
T
F1
F2
…
T + δ
NULL
CONSISTENT
CONSISTENT

## Slide 26: Snapshot consistency
 | Tamper resistance | Performance isolation | Snapshot consistency
Virtualization |  |  | 
Co-processor |  |  | 
Snapshot should faithfully represent target’s state at a given instant in time
Physical Memory
Hardware
Operating
System
F1
F2
…
T
T + δ
Co-processor cannot pause target. Snapshot may contain pages obtained at different instants in time
INCONSISTENT

## Slide 27: Introducing SnipSnap
 | Tamper resistance | Performance isolation | Snapshot consistency
Virtualization |  |  | 
Co-processor |  |  | 
SnipSnap |  |  | 
New hardware-based design for memory snapshotting.
Proposed deployment? Via die-stacked manufacturing.

## Slide 28: Die-stacked chip
Picture courtesy of AMD
CPU and
Memory controller
On-chip memory
(high-speed)

## Slide 29: Die-stacked chip
Picture courtesy of AMD
CPU and
Memory controller
On-chip memory
(high-speed)
Memory bus
Traditional (off-chip)
DRAM memory
Notes: Design space of methods to use the on-chip memory still a topic of active debate in the computer architecture community.

## Slide 30: Our use of die-stacking
On-chip DRAM treated as a page-granularity cache of off-chip DRAM memory
  Every address accessed by the CPU will result in the page frame being fetched to on-chip DRAM
Cache of off-chip
DRAM memory
Off-chip DRAM
On-chip DRAM
Memory controller
Crypto logic
CPU
Memory bus

## Slide 31: Triggering snapshot acquisition
On-chip DRAM
Memory controller
Crypto logic
CPU
Trigger = Device that communicates to the CPU to enter snapshot acquisition mode:
Physical device attached to South/NorthBridge that sends a non-maskable interrupt
NIC with Wake-on-LAN-like feature
Off-chip DRAM
Memory bus

## Slide 32: Snapshot acquisition mode
Memory controller
Crypto logic
CPU
Memory controller splits on-chip DRAM into two parts:
  Cache of off-chip DRAM memory
  Copy-on-Write (CoW) area
Cache
CoW
1
Off-chip DRAM
Memory bus

## Slide 33: Snapshot acquisition mode
Memory controller
Crypto logic
CPU
Hardware brings one page frame of off-chip DRAM at a time to on-chip DRAM cache
Cache
CoW
Fi
Fi
2
Off-chip DRAM
Memory bus

## Slide 34: Snapshot acquisition mode
Memory controller
Crypto logic
CPU
Crypto logic digitally signs contents of page:
  Random nonce used to prevent replay attacks
  Same nonce used for all pages in snapshot
Cache
CoW
+ Page#
+ Rand#
Fi
3
Off-chip DRAM
Memory bus

## Slide 35: Snapshot acquisition mode
Memory controller
Crypto logic
CPU
Hardware instructs OS to write signed page to external medium:
  Even if OS is infected, it cannot cheat, since integrity of page is protected by the hardware
Cache
CoW
Disk
4
+ Page#
+ Rand#
Fi
Off-chip DRAM
Memory bus

## Slide 36: Snapshot acquisition mode
CPU continues to execute concurrently:
  If it writes to page Fj that has not yet been copied  Memory controller makes a copy of the original page in the Copy-on-Write area
  When hardware ready to snapshot Fj, copy created from Copy-on-Write area
Memory controller
Crypto logic
CPU
Memory bus
Cache
CoW
5
Fj
Off-chip DRAM
Fj

## Slide 37: At conclusion of acquisition
Consistent snapshot of off-chip memory at instant when acquisition was initiated
Snapshot is tamper-resistant even to a corrupted OS
Obtained without pausing target machine
+ 0
+ R
F0
+ 1
+ R
F1
+ N
+ R
FN
…
Notes: If OS attempts to hide malicious activity, will be evident because CoW will capture original page.

## Slide 38: Security analysis
Malicious OS cannot:
  Corrupt pages in snapshot: Integrity
  Hide pages from snapshot: Completeness
  Replay old snapshot: Freshness
  “Clean” itself during snapshot acquisition because Copy-on-Write stores original page: External control
Verified SnipSnap’s design using the TLA+ model checker [Lamport]
+ 0
+ R
F0
+ 1
+ R
F1
+ N
+ R
FN
…
Notes: If OS attempts to hide malicious activity, will be evident because CoW will capture original page.

## Slide 39: Evaluation
Hardware emulator using a NUMA system.
Evaluated:
  Memory-intensive workloads
    canneal, dedup, memcached, graph500, mcf, cfar10, mnist
  Effectiveness of performance-isolation claim
  Time to procure full snapshot of memory

## Slide 40: Application performance with virtual machine-based snapshotting
Chart: DRAM size
| 512M | 2G | 8GB
net-100 | 1.0366 | 1.1029 | 1.5958
net-10 | 1.0839 | 1.236 | 2.3659
ssd | 1.0999 | 1.281 | 2.6264

## Slide 41: Application performance with SnipSnap-based snapshotting
Chart: DRAM sizes
| 512M | 2G | 8GB | 512M | 2G | 8GB | Virtual machine | SnipSnap
net-100 | 1.0366 | 1.1029 | 1.5958 | 1.0244 | 1.0392 | 1
net-10 | 1.0839 | 1.236 | 2.3659 | 1.0692 | 1.1606 | 1
ssd | 1.0999 | 1.281 | 2.6264 | 1.084 | 1.199 | 1

## Slide 42: Thank you
Vinod Ganapathy
Google “Secure, Consistent, High-Performance Memory Snapshotting” for a copy of the paper